## Slide 1: RoboNUI Design
Jon Eisen
Thor Kirkby

## Slide 2
RoboNUI System Architecture
Kinect Adapter
Robotics Adapter
Core Business Logic
GUI
Record/Playback

## Slide 3: RoboNUI Software Layer Design
Microsoft Visual C# .NET Framework
Microsoft Kinect Drivers
Microsoft Windows 7
LynxMotion Servo Drivers
Microsoft Kinect SDK
Windows Voice Recognition Library
Kinect Adapter Assembly
Servo Adapter Assembly
Record / Playback Assembly
GUI Assembly
RoboNUI Core Business Logic Assembly

## Slide 4: Requirements
The robot moves along with the motion of the controller.
  The Kinect Adapter measures the angles of each joint of the controller.
  The Kinect Adapter can identify the angle of each joint of the robot.
  The robot’s servos move at a pace consistent with general use of this system.
  The robot should have a range of motion consistent with normal human motion.
The controller should be able to use voice commands.
  The Kinect Adapter should be able to distinguish which controller spoke.
  The Kinect Adapter should be able to recognize simple speech phrases to allow voice commands.
  The Kinect Adapter should be able to switch primary controllers on a voice command.
The system should allow recording and playback of motions.
  The Record/Playback should listen to commands sent to the robot.
  The recorded commands should be stored in a minimal text format.
  Playback should mimic the robot’s movements during the recording phase exactly.
The GUI should be helpful and minimal.
  The GUI should display a skeletal view of the controllers.
  The GUI should display a view of the robot’s current state.
  The GUI should allow for controller switching.
  The GUI should allow for control of record/playback.

## Slide 5: Component-Based Architecture
Kinect Adapter Assembly
Skeletal Joint Monitor
Voice Command Interpreter
Servo Adapter Assembly
Robotic Arm Servo Controller
Robotic Marionette Servo Controller
RoboNUI Core Business Logic Assembly
State Manager
Joint-Angle Translator
GUI Assembly
GUI
Record / Playback Assembly
Recorder
Playback

## Slide 6: RoboNUI Software Model
GUI
State Manager
Joint-Angle Translator
Skeletal Joint Monitor
Voice Command Interpreter
Robotic Arm Servo Controller
Robotic Marionette Servo Controller
Recorder
Playback

## Slide 7: RoboNUI Software Model Primary Control Path
Kinect Drivers send raw data
Requested Joints are passed to the JAT
The Recorder records exact commands send to the servo controllers
The angles are then converted into servo commands
Joints are translated into Robotic Angles
Only one servo controller is on at any one time
Recorder
Playback
Joint-Angle Translator
Skeletal Joint Monitor
Robotic Arm Servo Controller
Robotic Marionette Servo Controller

## Slide 8: RoboNUI Software Model State Management
GUI
State Manager
Skeletal Joint Monitor
Voice Command Interpreter
Recorder
Playback
The SJM or Playback component are enabled and disabled mutually exclusively
Record and Playback are controlled by the State Manager
The VCI or GUI can send commands to the State Manager

## Slide 9: Schedule
Turn 1 - Core
SJM – Implement the monitoring of Joints based on a list given
JAT – Implement Joint Translation to robot angles based on robot configuration
Turn 2 - Control
SM – Implement control of the primary path of data (on/off, selection of data feeds)
GUI – Implement 3 parts [skeletons, robot state, control buttons & connected lights]
Turn 3 - Extended
R/P – Create a text format for record and playback. Implement store and load functionality, as well as streaming of robot commands
Update other components to work with R/P: SM, GUI, VCI
RSC – Implement one RSC (arm or marionette)
SM – Stub this such that the system turns on when executed
VCI – Implement voice commands as alternate to GUI, selection on controller
Open Development time / Buffer
August September October
8/23
9/13
10/4
7/27